## Slide 1: Digital transmission & encoding techniques

## Slide 2: Line coding

## Slide 3: Signal level versus data level

## Slide 4: Conversion methods
Electrical signals can be of various types
Analog , Digital

## Slide 5: Digital to digital conversion ( encoding )

## Slide 6
A signal has two data levels with a pulse duration of 1 ms. We calculate the pulse rate and bit rate as follows
  Pulse Rate = = 1000 pulses/s
  Bit Rate = PulseRate x log2 L = 1000 x log2 2 = 1000 bps
If signal has 4 data levels
  Bit Rate = PulseRate x log2 L = 1000 x log2 4 = 2000 bps

## Slide 7: Line coding schemes

## Slide 8
Unipolar encoding uses only one voltage level.

## Slide 9: Unipolar encoding
The average amplitude of unipolar signal is non zero
1 is encoded as +ve value
0 is encoded as zero
For non chaining signal beginning & end of each bit can not be determined

## Slide 10: Polar
It uses two voltage level (+ve , -Ve)
Average voltage level on the line is reduced
DC component problem can be solved

## Slide 11: Polar encoding techniques

## Slide 12: Non return to zero
In this technique the level is either +ve or negative
Two different type
NRZ-L
  In NRZ-L the level of the signal is dependent upon the state of the bit.
  +Ve represented as 1 and -ve represented as 0 or vice versa
  Clock synchronization
NRZ I
  In NRZ-I the signal is inverted if a 1 is encountered.
  The signal transition can be used for clock synchronization

## Slide 13: NRZ L & NRZ I
A good encoding technique must contain provision for synchronization

## Slide 14: RZ encoding
Ensure that there is signal change for every bit
This requires three voltage level : +Ve zero, & negative

## Slide 15: Biphase
The signal changes at the middle of the interval but does not return to zero
Manchester encoding : inversion at middle of each bit interval
Negative to positive represent 1
+ve to negative represent 0
Differential Manchester : presence or absence of additional transition at the beginning of interval is used for identifying the bit
DM require two transition to represent zero and one for Binary 1

## Slide 16: Bipolar
It uses three voltage levels
+ve , -Ve & Zero
  Zero level represents the binary zero
  1 is represented by alternating +ve & -Ve voltages

## Slide 17: Bipolar AMI

## Slide 18: Block Coding

## Slide 19: Substitution in block coding

## Slide 20: 4B/5B encoding
Data | Code | Data | Code
0000 | 11110 | 1000 | 10010
0001 | 01001 | 1001 | 10011
0010 | 10100 | 1010 | 10110
0011 | 10101 | 1011 | 10111
0100 | 01010 | 1100 | 11010
0101 | 01011 | 1101 | 11011
0110 | 01110 | 1110 | 11100
0111 | 01111 | 1111 | 11101

## Slide 21
Data | Code
Q (Quiet) | 00000
I (Idle) | 11111
H (Halt) | 00100
J (start delimiter) | 11000
K (start delimiter) | 10001
T (end delimiter) | 01101
S (Set) | 11001
R (Reset) | 00111