## Slide 1: Network basics

## Slide 2: High availability network

## Slide 3: High availability network
We notice that there exists multiple paths from various switches and some kind of loop is formed among them
In network loop can cause severe issues
Loops can be formed for verity of reason
  To provide redundancy
  Loop can be formed due to mistake (unintentional )
  Loops can result into
    Broadcast storm
    Bridge table corruption

## Slide 4: Broadcast creates a feed back loop

## Slide 5: Bridge table corruption

## Slide 6: Spanning Tree Protocol
STP is loop avoidance protocol
Key concept
  Bridge ID
  Path cost
  The default bridge priority is 32768

## Slide 7: Path cost
802.1D originally defined cost as 1000Mbps divided by bandwidth of the link

## Slide 8: STP decision sequence
When creating loop free topology, STP always uses four step decision sequence
  Lowest root BID
  Lowest path cost
  Lowest sender BID
  Lowest Port ID
Bridges generate & pass special frame Known as BPDU (Bridge protocol data unit )
It considers all BPDU received on port, and uses the best BPDU
All port send BPDU every 2 second and stop once they receive better BPDU
If more attractive BPDU stops arriving from neighbour for a period of more than 20 seconds the local ports once again can resume sending BPDU
Two types of BPDU
  Configuration BPDU
  Topology change notification ( TCN ) BPDU

## Slide 9: Three steps of STP convergence
Elect one root bridge
Elect root port
Elect designated port

## Slide 10: BPDU layout

## Slide 11: Sample network

## Slide 12: Elect root bridge

## Slide 13: Elect root port
Every non root bridge must select one root port
Root port is port that is closest to root bridge

## Slide 14: Elect designated Port
Every segment has a designated port and all traffic is sent or received by designated port only

## Slide 15: Frame header changes through router
Frame Exchange in a routed network

## Slide 16: Broadcast and collision domain in routed network

## Slide 17: Network
OSI ( Open Standard Interconnect ) Model Has seven layers
  Physical, Data Link, Network, Transport, Session, Presentation, and Application.
Fibre Channel does not follow this model, the protocol has been broken into five layers
  FC-0, FC-1, FC-2, FC-3, and FC-4
  FC-0 to FC-2 contains the physical description of Fibre Channel defined in the FC-PH
  FC-3 and FC-4 describe the interface with other applications

## Slide 18: What is Channel ?
channel is a closed, direct, structured, and predictable mechanism for transmitting data between relatively few entities.
It provides a direct or switched point-to-point connection between the communicating devices.
once a channel is set up, there is very little decision making needed enabling hardware-intensive environment and transports data at the high speed with low overhead.
Channels are commonly used to connect peripheral devices such as a disk drive, printer, tape drive, etc. to a workstation.
Common channel protocols are Small Computer System Interface (SCSI) and High Performance Parallel Interface (HIPPI).

## Slide 19: Network
Networks are aggregations of distributed nodes(like workstations, file servers or peripherals) with there own protocol that support interaction among these nodes.
Networks are unstructured and unpredictable
Networks are able to automatically adjust to changing environments and can support a larger number of connected nodes.
Require decision making in order to successfully route data from one point to another.
Networks have relatively high overhead since they are software-intensive
networks inherently slower than channels.
Examples of common networks are Ethernet, Token Ring, and Fiber Distributed Data Interface (FDDI)